## Slide 1: Operating Systems
Chapter 1

## Slide 2: Operating System
Collection of programs that
  Acts as an interface between user and the machine
  Provides services to system users
  Provides an environment for users to develop, debug, and maintain their programs
  Allocates system resources so as to achieve their maximum utilization

## Slide 3: Basic elements
Major hardware components of a computer system are:
  Processor
  Memory
  Input/output modules
  System bus

## Slide 4: Processor
Usually known as the Central Processing Unit (CPU)
Capable of performing simple arithmetic operations
  The part of processor that performs these operations is known as ALU (Arithmetic Logic Unit)
Controls operations of various computer components
  The part of processor performing this operation is called the Control Unit

## Slide 5: Main Memory
Used for storage and retrieval of data and instructions
Main memory is volatile
  Memory contents are lost when the power is turned of
  (Memory content of a disk unit are not lost when power is turned of)
Also known as real or primary memory

## Slide 6: Input/Output Devices
These devices are used for moving data from outside world to the computer and from the computer to the outside world, e.g.,
  Keyboard
  Terminal
  Printer
  Hard drive
  Communication equipment

## Slide 7: System Bus
System bus allows communication to take place amongst processor, computer main memory, and input/output devices

## Slide 8: Computer hardware
Central Processing
Unit
(PC, IR, MAR, MBR, I/O-AR, I/O-BR)
Memory
I/O
Module1
I/O
Module2
…
System Bus

## Slide 9: Microprocessors
Invention that brought about desktop and handheld computing
Processor on a single chip
Fastest general purpose processor
Multiprocessors
Each chip (socket) contains multiple processors (cores)

## Slide 10: Graphical Processing Units
A GPU is a set of multiprocessors
Provides efficient computation on arrays of data using single-instruction multiple data stream
Used for general numerical processing, simulations for games, computation on large spreadsheets, etc.

## Slide 11: Instruction Execution
A CPU is programmed to work as follows:
loop{
IR = Memory[PC]; /*fetch*/
increment PC;
execute instruction; /*execute*/
} until instruction = halt;

## Slide 12: Instruction Fetch & Execute
The program counter (PC) holds address of the instruction to be executed next
The processor fetches the instruction from memory location with address in PC
PC is incremented after each fetch to point to the next instruction in memory.

## Slide 13: Basic Instruction Cycle
Fetch Next Instruction
Execute
Instruction
START
HALT

## Slide 14: Instruction Fetch & Execute
The program counter (PC) holds address of the instruction to be fetched next
  PC is incremented appropriately after each fetch
The processor fetches the instruction memory

## Slide 15: Instruction Register
The fetched instruction is loaded into a CPU register called Instruction Register (IR)
Processor interprets the instruction in IR and performs the action indicated by the instruction
The instruction can be one of the following types:
  Processor-memory
  Processor-I/O
  Data processing
  Control

## Slide 16: Interrupts
A mechanism by which various devices send a signal to CPU
An important part of a computer architecture.
Provided to improve processor utilization
  Most I/O devices much slower than the processor
  Processor must wait for the device
  Wasteful use of the processor
It interrupts the normal sequencing of the processor

## Slide 17: Common classes of Interrupts
Program – generated by some condition that results when an instruction is executed
  Arithmetic overflow, division by zero, illegal instruction, illegal reference
Timer – generated by the timer within the processor
I/O – generated by an I/O controller
Hardware failure
  Power failure
  Memory parity error

## Slide 18: Interrupt processing
An interrupt is issued
Action taken by hardware
  Processor finishes execution of current instruction
  Processor signals acknowledgement of interrupt
  Partial status of the running program is saved
  Processor loads new PC value based on interrupt

## Slide 19: Interrupt processing (2)
Action taken by Software
  Before serving the interrupt
    Save remainder of process state information
    Service the interrupt
  After serving the interrupt
    Restore process state information saved by software
    Restore old process status information and the old PC

## Slide 20: Multiple interrupts
What to do if an interrupt occurs while processing an interrupt
Two approaches
  Disable interrupts while an interrupt is being processed
    Does not take into account time-critical needs; example: data arrival on communication lines
  Use a priority scheme
    Allows a higher priority interrupt to be handled while a lower priority interrupt is being serviced.

## Slide 21: Memory Hierarchy
Programs must be in main memory to be executed
Main memory is the only large memory a processor can access directly
Major constraints in memory
  size
  Speed
  Cost
Memory must be able to keep up with the processor
The memory cost must be reasonable in relation to the other components

## Slide 22: Memory relationship
Faster access time  greater cost per bit
Greater capacity  smaller cost per bit
Greater capacity  slower access speed

## Slide 23: The Memory Hierarchy (2)
Going down the hierarchy:
  Decreasing cost per bit
  Increasing capacity
  Increasing access time
  Decreasing frequency of access to the memory by the processor

## Slide 24: The Memory hierarchy (3)
Hierarchy based on speed and cost
  Registers
  Cache
  Main memory
  Electronic disk
  Magnetic disk
  Optical disk
  Magnetic tapes

## Slide 25: Performance of Simple two level memory
Supplement a smaller, more expensive, faster memory with a larger, less expensive, slower memory.
The CPU can directly access the smaller, more expensive, faster memory.
Access to other memory is through the smaller, more expensive, faster memory
Success of the scheme depends on finding most of the needed data in the smaller memory.
  This is possible to achieve because of the locality of programs

## Slide 26: Principle of Locality
Memory referenced by the processor tend to cluster
Data is organized so that the percentage of accesses to each successively lower level is substantially less than that of the level above
Can be applied across more than two levels of memory

## Slide 27: Secondary Memory
Also known as Auxiliary Memory
  Cannot be accessed directly by the CPU
  External
  Very large compared to main memory
  Used to store program and data files

## Slide 28: Cache Memory
Invisible to the OS
Interacts with other memory management hardware
Processor accesses main memory at least once per instruction cycle.
  Processor execution is limited by memory cycle time
Cache memory is used to exploit the principle of locality with a small, fast memory

## Slide 29: Cache principle
Cache memory contains a copy of a portion of main memory
Processor first checks cache
If not found, a block of memory is read into cache
Because of locality of reference, it is likely that many of the future memory references will be to other data brought into cache as a block
May employ multiple level of cache

## Slide 30: Cache Design features
Number of cache levels
Cache size
Block size
Mapping function
Write policy
Replacement policy

## Slide 31: Cache and block size
A small amount of cache has a significant impact on performance
Block size: The unit of data exchanged between cache and main memory

## Slide 32: Mapping function
The mapping function determines which cache location the memory block will occupy
Two constraints affect design
  When one block is read in, another may have to be replaced
  The more flexible the mapping function, the more complex is the circuitry required to search the cache

## Slide 33: Replacement algorithm
Least Recently Used (LRU) algorithm
  An effective strategy is to replace a block of data that has been in cache and has not been referenced for the longest time
  Hardware mechanisms are needed to identify the last recently used block
    Chooses which block to replace when a new block is to be loaded into the cache

## Slide 34: Write policy
Dictates when the memory write operation takes place
  Can occur every time the block is updated
  Can occur when the block is replaced
    Minimizes write operations
    Leaves main memory in an obsolete state

## Slide 35: I/O Techniques
When the processor encounters an instruction relating to I/O, it executes that instruction by issuing a command to the appropriate I/O module
Three techniques:
  Programmed I/O
  Interrupt driven I/O
  Direct memory access (DMA)

## Slide 36: Programmed I/O
The I/O module performs the requested action, then sets the appropriate bits in the I/O status register
The process periodically checks the status of the I/O module until it determines the instruction is complete
With this technique, the performance level of the entire system is severely degraded

## Slide 37: Interrupt-Driven I/O
Processor issues an I/O command to a module and then goes to do some other useful work
The I/O module will then interrupt the processor to request service when it is ready to exchange data with the processor
The processor executes the data transfer and then resumes its former processing
More efficient than programmed I/O but still requires active intervention of the processor to transfer data between memory and an I/O module

## Slide 38: Interrupt-driven I/O drawbacks
Transfer rate is limited by the speed with which the processor can test and service a device
The processor is tied up in managing an I/O transfer
  A number of instructions must be executed for each I/O transfer

## Slide 39: Direct Memory access
Performed by a separate module on the system bus or incorporated into an I/O module
When the processor wishes to read/write data it issues a command to the DMA module containing the following information:
  Request type (read or write)
  The address of the I/O device
  The starting location in memory to read/write
  The number of bytes to be read/written

## Slide 40: Direct memory access
Transfer the entire block of data directly to and from memory without going through the processor
  Processor is involved only at the beginning and end of the transfer
  Processor executes more slowly during a transfer when processor access to the bus is required.
More efficient than interrupt-driven or programmed I/O

## Slide 41: Symmetric Multiprocessors (SMP)
A stand-alone computer system with the following characteristics:
  Multiple processors of comparable capability
  Processors share the same main memory
  Processors are interconnected by a bus or other internal connection scheme
  Processors share access to I/O devices
  All processors can perform the same functions
  The system is controlled by an integrated operating system that provides interaction between processors and their programs at the job, task, file, and data element levels

## Slide 42: SMP advantages
Increased throughput: Yields greater performance if work can be done in parallel
Economy of scale: A multiprocessor system costs less than an equivalent multiple single processor systems.
Increased reliability: The failure of a single processor does not halt the machine
Incremental growth: An additional processor can be added to enhance performance

## Slide 43: Multicore computer
Also known as chip multiprocessor
Combines two or more processors (cores) on a single piece of silicon (die)
  Each core consists of all the components of an independent processor
In addition, multicore chips also include 2-level cache, and in some cases 3-level cache

## Slide 44: Summary
Basic elements of a Computer system:
  Processor, main memory, I/O modules, system bus
  Instruction execution
    Processor-memory, processor-I/O, data processing, control
  Interrupt/interrupt handling
  Memory hierarchy
  Cache/cache principles and designs
  Multiprocessor/multicore